ETEE 1223

Homework 13

17.	The load on a 120V, 60Hz supply is 5KW (resistive), 8KVAR (inductive), and 2KVAR (capacitive).

- Find the total kilovolt-amps.

- Determine the Fp of the combined loads.

- Find the current drawn from the supply.

- Calculate the capacitance necessary to establish a unity power factor.

- Find the current drawn from the supply at unity power factor, and compare it to the uncompensated level.

18.	The loading of a factory on a 1000V, 60Hz system consists of the following:

20KW heating (unity power factor)

10KW of induction motors (at 0.7 lagging power factor)

5KW lighting (0.85 lagging power factor)

- Establish the power triangle for the total loading on the supply.

- Determine the power-factor capacitor required to raise the power factor to unity.

- Determine the change in supply current from the uncompensated to the compensated system.