ETEE 1223

Homework  2 (3-phase)

A delta-connected 3-phase load has impedance 9 + j12 Ω/φ.  It is connected to a distribution line of impedance 1 + j2 Ω/φ. At the sending end of the line a delta connected source of impedance 0.5 + j1 Ω/φ has internal voltage of magnitude 1000V.  The system has positive phase sequence.  Use the internal source voltage Vab’ as reference.

- Construct the single phase equivalent circuit.

- Find the line currents IaA and IbB.

- Find the magnitude of the line voltage at the source terminals.

- Find the three phase currents flowing in the load.

- Find the total average power delivered by the source.

- Find the total average power and reactive power absorbed by the load.

- Find the total average power lost in the transmission line.