ETEE 1223

Homework 12

19-2. For the network below:

  - Find the average power delivered to each element

  - Find the reactive power for each element.

  - Find the apparent power for each element.

  - Find the total number of W, VAR and VA, and the power factor Fp of the circuit.

  - Sketch the power triangle.

19-4. For the system below:

  - Find PT, QT and ST

  - Determine the power factor Fp.

  - Draw the power triangle.

  - Find Is.

19-5. For the system below:

a. Find PT, QT and ST

b. Determine the power factor Fp.

c. Draw the power triangle.

d. Find Is.

19-6. For the circuit below:

  - Find the average, reactive and apparent power for the 20Ω resistor.

  - Repeat part (a) for the10 Ω inductive reactance.

  - Find the total number of watts, volt-amps reactive, and volt-amps, and the power factor Fp.

  - Find the current Is.

19-7. For the circuit below:

  - Find the average power delivered to each element.

  - Find the reactive power for each element.

  - Find the apparent power for each element.

  - Find PT, QT and ST and Fp for the system.

  - Sketch the power triangle.

  - Find the current Is.

19-10. An electrical system is rated 10 KVA, 200V at a 0.5 leading power factor.

  - Determine the impedance of the system in rectangular coordinates.

  - Find the average power delivered to the system.

19-11. An electrical system is rated 5 KVA, 120V at a 0.8 lagging power factor.

- Determine the impedance of the system in rectangular coordinates.

- Find the average power delivered to the system.

19-15. For the system below:

- Find the total number of watts, volt-amps reactive, and volt-amps, and Fp.

- Find the voltage E.

- Find the type of elements and their impedance in each box (Assume that the elements within each box are in series)

# Text boxes

Cancelled

Cancelled

Cancelled